VALLEY PLATING, INC.

# RESTRICTION ON HAZARDOUS SUBSTANCES

Key notes concerning RoHS (Restriction on Hazardous Substances) mandated by the European Union.

By July 1, 2006, new electrical and electronic equipment put on the market shall not contain lead, mercury, cadmium, and hexavalent chromium.

This affects any company that manufactures components for the electrical and electronics industry whose customer base includes member states of the European Union.

Customers contracting Valley Plating regarding compliance should be informed as follows:

Any parts requiring the following finishes can be assumed as "not" being RoHS compliant:

-     Parts requiring Cadmium Plate

-     Black Oxide requiring a post Hexavalent chrome seal IAW MIL-DTL-13924 & HP4-50 or when

Specified on purchase order.

Clear and Yellow Chemical Conversion Coatings on aluminum whereby specifications mandate the

use of solutions containing Hexavalent chrome.

(Applicable specs: AMS 2473, AMS 2474, DPS 9.45, HP4-57, HS 240, MIL-DTL-5541 ty.1, MIL-STD-171, PN 14.12, PWA 830 Code 2, SS8486 ty.1, or when specified on purchase order)

Note:  Valley Plating offers a Trivalent Chemical Conversion Coating on aluminum

that is RoHS compliant.

- Silver plated parts requiring Anti-Tarnish. (Applicable specs: QQ-S 365 Grade A, ASTM B700 Class A, HS 519 Class S, or when specified on purchase order)

- Types 1, 2, & 3 Anodize requiring Post Sodium Dichromate Sealing.

(Applicable specs: AMS 2471, CPS 1000 Class 1D, CPS 1000-01 Class 1D, PWA 830 code 7, PWA-S-2471, or when specified on purchase order)

## Paint and Dry Film Finishes

- Everlube 642 (Pb)				PWA 474

- Fel-Pro C-200 (Pb)				PWA 586

- Lube-Lok 1000 (Pb)				HS 248 TY A3

- Lube-Lok 5306 (Pb)				MIL-L-46010 TY I

- Lubrabond 220 (Pb)				MIL-L-23398 TY I & II

- MIL-PRF-23377 TY I, Yellow (CR)	MIL-PRF-23377 TY 1

- Molydag 254 (Pb)				A50TF147-S11; CL A & C

- Molykote 3400A (Pb)			Proprietary

- Sandstrom 9A (Pb)				AS 5272 TY II

- Zinc Chromate Yellow Primer (CR) 	TT-P-1757 TY I; CL C

Note:	Within the European mandate there are some exceptions relating to aerospace/military components

which is the responsibility of the customer to determine applicability.

Revised: 06/12/20